Navigation Committee

29 May 2002

STANDARD APPROACHES AND DEPARTURES

Potential Elements

Approaches:

- prescribe approach altitudes that maintain a 3-degree glide slope from at least 5000 feet above field elevation to touchdown on all approaches; eliminate current exceptions

- refine extended flight tracks and way points to follow minimal-impact corridors as closely as possible throughout Louisville airspace - specifically, interstate highways and the river

- based on the above, set final approach fixes at or near the river in the north, and I-265 in the south, and grant visual clearances only after arriving aircraft pass those fixes

- include noise abatement flight procedures in standard approach descriptions; in particular, include provisions to implement a 'decelerating approach' procedure for arrivals

Departures:

- set departure procedures to prescribe turns at specific points, rather than altitudes, so as to follow specific flight tracks

- refine extended flight tracks and way points to follow minimal-impact corridors as closely as possible throughout Louisville airspace – specifically, interstate highways and the river

- based on the above, set departure way points at or near the river in the north, and I-265 in the south, based on specific navigational fixes rather than radar headings

- include noise abatement flight procedures in standard departure descriptions to fit the runway environment; presumably close-in procedures for northbounds, and distant procedures for southbounds